## Slide 1: RADAR Altimetry & Scatterometry

## Slide 5
Range resolution – examples
Rr = t c/2cos(g)

## Slide 6
Azimuth resolution

## Slide 7
Azimuth resolution – examples
Ra = (0.7)(S)(l)/D

## Slide 8: Altimetry

## Slide 10
Lifetime 1992-2006
Altitude 1335 km
Pulse length 3.125 nsec
Repeat time 9.9156 days
Resolution 25 km
Frequency 13.65 GHz
Follow-on Missions
Jason-1 2001
Jason-2 2008
Jason-3 2013

## Slide 12
1 Ocean
2 Reference ellipsoid
3 Local plumb line
4 Continent
5 Geoid
- Geoid height given relative to reference ellipsoid
- Reference ellipsoid is best fit to geoid
- Sea surface height measured relative to geoid (<100 m)
Using a sphere would result in height differences between geoid as large as 20 km due to equatorial bulge

## Slide 13
Instead of the GEOID, measurements can be made relative to repeated orbits

## Slide 14: Scatterometry

## Slide 15
Scatterometers and their characteristics
Scatterometer Period Spatial Scan Operational
in Service Resolution Characteristics Frequency
SeaSat-A July 7, 1978– 50 km with two sided, Ku band
Oct 10, 1978 100 km spacing double swath (14.6 GHz)
ERS-1 July 1991 – 50 km one sided, C band
May 21, 1997 single swath (5.3 GHz)
ERS-2 May 21, 1997– 50 km one sided, C band
Current single swath (5.3 GHz)
NSCAT Sep 15, 1996 – 25 km, and two sided, Ku band
Jun 30,1997 50 km double swath (13.995 GHz)
SeaWinds on Jul 19, 1999 - 25 km conical scan, Ku band
QuikSCAT Nov 23, 2009 one wide swath (13.995 GHz)
SeaWinds on Apr 10, 2003 25 x 6 km conical scan Ku band
ADEOS II Oct 24, 2003 one wide swath (13.995 GHz)
ASCAT May 2007- 50 km conical scan C band
Current one wide swath (5.255 GHz)
RapidScat on Sep 20, 2014- 16 km conical scan Ku band
Int. Space Sta. Current 1000 km swath (13.4 GHz)

## Slide 19
Four different viewing angles