Orbits, Angles and Resolution

# Important angles

Zenith (theta)

Nadir (180-theta)

Elevation (90-theta)

Scan angle, Angular field of view (scan angle*2)

Azimuth angle

# Spatial resolution and resolving power

Define resolving power or resolution

The ability to perceive two adjacent objects as being distinct

A function of many things

Size

Distance

Sensor characteristics

Object shape

Object color

Contrast characteristics

Dwell time – how long you can look at an object

Angular resolving power

The key is the angle

Only angle is “constant” (its not really, it can change with contrast, etc.)

Minimum resolvable distance will change with distance from sensor

The radian system of angular measurement

1 rad is the angle subtended by an arc which is the same length as the radius

So for 1 rad, L = r

This is convenient because the angle (in rads) is simply the ratio of L / r

i.e. if you know the distances, you know the angle!

If L is half of r, then the angle is 0.5 rad

If L is one quarter of r, then the angle is 0.25 rad

Calculation of angular resolving power

Use the eye as an example of a remote sensing system

It’s like a satellite sensor in important ways

Lens for focusing

Array of detectors

Optical systems have an inherent resolving power determined by their optics

Resolving power is a function of receptor cell size and image distance (from lens)

(Don't confuse r with the radius of the eye. r is the distance between the point where the two light rays converge on the lens and the receptor.  In a circle, these lines converge at the center, which defines the radius.  In our eye they converge at the edge of the circle, where our lens is.)

Equation for IFOV [IFOV(rad) =L / r]

The smaller the IFOV ( the higher the resolution

IFOV is a relative measure because its an angle, not a length

The angle relates the size of an object to its resolving distance

For an average person:

Receptor cell=4 µm (this is L)

Image distance within eye = 20,000 µm (this is r)

IFOV = L/r = 4/20,000 = 0.0002 rad = 0.2 mrad

Show how image distance is proportional to object distance

How big must L’ be to resolve at a distance of 30 m?

IFOV = L’/r’

L’ = IFOV • r’

L’ = 30 m • 0.0002 = 0.006 m = 0.6 cm

How does IFOV come into play when we’re looking at something?

Calculate IFOV for student’s eyes

IFOV(rad) = L mm/5000 mm

For L = 0.71 mm, IFOV = 0.142 mrad

For L = 0.83 mm, IFOV = 0.166 mrad

For L = 1.00 mm, IFOV = 0.200 mrad

For L = 1.25 mm, IFOV = 0.250 mrad

For L = 1.67 mm, IFOV = 0.334 mrad

Repeat calculation of IFOV for a lower contrast target

Use IFOV and satellite height to calculate size (L) of the ground resolution cell (pixel size)

Use SeaWiFS as an example (The IFOV for SeaWiFS is 1.6 mrad, its altitude is 705 km)

Solving for L, use the equation:

IFOV = L/r

1.6 mrad = L/705 km

0.0016 rad = L/705 km

L = 1.13 km

# Spectral resolution

Bandwidth

# Scanning satellite systems

Scan angle

Angular field of view = 2 • scan angle

Calculation of ground swath width from angular field of view

An example from SeaWiFS

ground swath width = 2 • r • tan(scan angle)

Altitude = 705 m

Scan angle = 58.3°, tan(58.3°) = 1.62

ground swath width = 2 • 705 • 1.62 = 2282 km

How big are pixels at nadir?

(L=IFOV • r) = 0.0016 rad • 705 km = 1.13 km

How big are pixels at swath edge?

r = altitude/cos(scan angle)

r = 705 km/cos(58.3°) = 705km/0.525 = 1341 km

Pixel size (L) = IFOV • r

L = 0.0016 rad • 1341 km = 2.15 km

Cross-track scanning systems

What is the dwell time for a cross track scanner?

(= scan rate per line/# cells per line)

What do you need to know?

Satellite speed for SeaWiFS (distance traveled/orbit time)

Distance traveled = 2 • pi • r = 2 • pi • (6378+705) km

=44,503 km

Orbit time = 99 minutes

=449.5 km/min

Width of scan line (1.13 km for SeaWiFS)

Time per scan line = 1.13 km/449.5 km/min = 0.0025 min

Time per pixel

= (2282 km/swath)/(1.64 km/pixel) = 1391 pixels

= 0.0025 min/(1391 pixels) = 1.08e-4 sec/pixel

What about other scanning systems?

Along track (push broom)

Have multiple detectors

Longer dwell time (cell dimension/satellite velocity)

At the same ground speed, cross track scanners sample 2000x more pixels

Attributes 	Cross-track 	Along-track

Angular field of view	Wider	Narrower

Mechanical system	Complex	Simple

Optical system	Simple	Complex

Dwell time	Shorter	Longer

Side scanning systems (active)

Similar to cross-track systems

Resolution and data quality ultimately related to signal strength

# What determines signal strength?

Energy flux

Altitude

Spectral bandwidth of detector

IFOV

Dwell time

# Multi-spectral systems

# Orbits

Geostationary, geosynchronous (GOES)

Sun-synchronous

Polar orbiting

Repeat times - SeaWiFS 1-day

Crosses equator at noon + 20 min on descending orbit

Orbits at a 99° angle.  Why?

The earth moves 2755 km each orbit (40073 km/24 hr = 2755 km/99 min)

The orbit is angled to bring swaths closer together to prevent big gaps.

The larger the angle, the more the swaths overlap

At an angle of 180°, satellite would orbit the equator and swaths overlap completely

# Getting the data from the satellite to the ground

Ground stations

On board recording capability